## Slide 1: An Educational Framework for AI-Driven RF Signal Processing on FPGA
Jude Eschete | Advisor: Dr. Bernard Yett | EE800

## Slide 2: Problem and Solution Overview
EE programs often teach FPGA, RF, embedded firmware, and ML separately, but industry failures happen at the interfaces.
Built a low-cost integrated platform: 3x STM32 + RFM95W LoRa nodes, Nexys A7 FPGA ingestion pipeline, host-side ML.
Curriculum is five modules (M1 to M5) with eight handouts each; Modules 1 to 4 were executed end-to-end on hardware.
Interceptor node adds button-gated PAUSE protocol for closed-loop intercept-and-act behavior on the same legal ISM channel.

## Slide 3: Key Results (Measured on Hardware)
FPGA pipeline closed timing at 100 MHz; 105,975/105,975 setup+hold endpoints met, 0 CDC violations.
Verification: 10/10 testbenches PASS, including byte-for-byte agreement vs Python reference on clean, mixed, and corrupted captures.
Dataset: 2,197 labeled rows from C1 (TX power), C2 (SF7 to SF10), and C5 (active stations), with 9-check audit PASS.
ML: 1-D CNN achieved 0.985 SF-task accuracy; live deployment classified 362 frames at 2.00 fps with 1.6 ms p99 host latency.

## Slide 4: Cross-Domain Integration Faults
Missing NVIC interrupt enable in M1 firmware caused 100% drop rate symptom at M2 FPGA ingestion.
Synchronous reset clause in M2 BRAM inference synthesized as 65k flip-flops instead of block RAM.
Missing SX1276 RegPaDac write in M1 broke +20 dBm link-budget monotonicity observed in M3 validation.
Session-confounded freq_error feature in M3 produced leakage and falsely perfect M4 test performance.
Each fault originated in one module and surfaced in another, directly exercising cross-domain debugging skills.

## Slide 5: Conclusion and Future Work
Delivered a 5-module integrated curriculum; Modules 1 to 4 were executed on real hardware with reproducible logs.
Demonstrated live three-task classification pipeline at 2 fps and 1.6 ms p99 inference latency.
Documented four cross-domain faults as evidence that integration reasoning is teachable and measurable.
Next: run full Module 5 cohort validation, recollect deferred C4 distance campaign, and expand optional C3 modulation classes.